## Slide 1: Intel Labs Workstream mTCP/DPDK Userspace Network Stack for Application Acceleration (Node.js) Gate-2: Phase Transition from PoC to Transfer
Muhammad Asim Jamshed & Christian Maciocco
Notes: This is a gate 2 talk titled “mTCP/DPDK Userspace Network Stack for Application Acceleration (Node.js).

## Slide 2: RAPID
Topic | Intel Labs Workstream Gate 2 Transition Review: mTCP/DPDK Userspace Network Stack for Application Acceleration (Node.js)
Recommenders | IL: Pranav Mehta, Christian Maciocco SSG: Uttam Pawar
Agreers | Monica Ene-Pietrosanu (Software Engineering Manager, SSG/OTC/DCSP)
Performers | Muhammad Asim Jamshed (IL), Christian Maciocco (IL), Uttam Pawar (SSG)
Inputers | Pranav Mehta, Christian Maciocco (IL)
Decider | Rich Uhlig (Managing Director, Intel Labs)
Decision | Recommend mTCP stack with extensions for Node.js transition from POC to Transfer Scope of the proposed transfer: mTCP version of node.js BU Recipient: SSG/OTC/DCSP Team
Notes: This is the RAPID table
Our goal is to transfer the node.js stack that is compatible with the mTCP stack (libc-wrapper version) once Gate 3 is finished
  mTCP-libc-wrapper is an mTCP branch that is compatible with Node.js project
    No change (in code) is required in legacy apps
    Transparent integration of the app to the stack

## Slide 3: Node.js
Node.js
Node.js Bindings (C++)
<socket, http parser…>
V8 (C++)
Libuv (C)
Cross platform asynchronous I/O event loop + worker thread pool + …
Node.js Application (JavaScript)
OS Kernel
JavaScript event-driven, non-blocking runtime engine
  Fast, scalable network application services
Widespread client base
Notes: Node.js is a fast scale-able server run time engine
The server application can be written in JavaScript
Node.js is widely being used across the industry. Some of its customers include LinkedIn, Uber, Netflix, Trello, NASA, Walmart and PayPal.
Node.js is composed of 4 components.
  1. The application section contains the JavaScript code that runs the server application logic.
  2. V8 is the open source module that interprets the JS code with the help of JavaScript runtime engine that converts JavaScript bytecode to machine language at run-time.
  3. Node.js bindings is the shim layer that acts as a go-between for the network I/O layer, file system I/O calls etc.
  4. libuv is a third party library that is responsible for I/O tasks including network communication

## Slide 4: Libuv’s Network Subsystem
Network I/O handled within libuv framework
  Follows event-driven model
Micro-benchmarks reveal network I/O consumes 45% CPU cycles
  Performance does not scale linearly with addition of CPUs
  Connection rate does not improve with increasing number of requests per sec
  Performance chokes for small flow sizes
  Node.js microbenchmarks: only 3 Mbps per Intel Broadwell CPU core
Linux kernel networking stack is the bottleneck
Notes: Network I/O events are handled by the kernel networking stack via the BSD socket interface.
Network subsystem proves to be the bottleneck (in terms of performance)
To make matters worse, the performance does not scale linearly with increase of CPUs
Connection rate drops as the request rate increases
Our micro-benchmark tests reveal that node.js only consumes 3 Mbps of networking bandwidth on a single Intel Broadwell CPU processing core.
We hypothesize that the Linux kernel networking stack is the bottleneck.

## Slide 5: Broken CPU Cache Locality
1. Broken locality
Per-core packet queue
Receive-Side Scaling (H/W)
Core 0
Core 1
Core 3
Core 2
Interrupt handler +
TCP state
management
accept() read() write()
Interrupt handling core != accepting core
Notes: We now explain the reasons behind Linux kernel networking stack’s slow performance. In this talk I am only going to discuss 2 salient issues.
First, we see that one core handles the RX interrupt and processes TCP-specific RX operations.
Since the interrupt handling core is different than the accepting core, there is a necessary L2/L3 cache miss (depending on CPU core configuration).
Modern Linux kernels allow interrupt #s to be affinitized to an arbitrary core. This means that one can assign the same core to run the application process as well as the interrupt service routine. However this still does not guarantee that the TCP state management also taking place in the same core (in the multi-core environment).

## Slide 6: Lack of Support for Batch Processing
2. Per packet, per system call processing
Inefficient per packet processing
Frequent mode switching Cache pollution
Per packet memory allocation
Inefficient per system call processing
accept(), read(), write()
Packet I/O
Kernel TCP
Application process
BSD socket
Linux epoll
Kernel
User
Notes: In the second example, we explain what happens when a packet arrives in the NIC
Each packet goes through an expensive (thick) kernel-resident networking stack. There is also a necessary kernel user space context switch. Memory allocation per packet as well as the amount of CPU cycles spent on packet processing in the stack (due to excessive memory copy operations) leads to frequent mode switching and CPU cache pollution.

## Slide 7: mTCP Background
TCP/IP stack: manages active network connections in the system; replaces kernel networking stack
  Ongoing project brought over to Intel Labs
Bypasses the kernel networking stack: major bottleneck
  Data plane Development Kit (DPDK), Netmap
Multi-core aware, highly parallelizable
  User space & uniform distribution of tasks across cores (RSS)
Run to completion model
Can operate at 10+ Gbps networks
Notes: mTCP is a user space TCP/IP stack that is built on the user space Intel DPDK suite. mTCP also works on top of Netmap driver.
It bypasses the kernel networking stack.
mTCP, like DPDK, is multi-core aware (which makes it highly parallelizable) and follows a run-to-completion model.

## Slide 8: Multicore Scalability
64B ping/pong messages per connection
Heavy connection overhead, small packet processing overhead
25x Linux, 5x SO_REUSEPORT
Chart: Multicore Scalability Test
| 1 | 2 | 4 | 6 | 8
Linux | 93658 | 139161 | 134583 | 83000 | 59549
REUSEPORT | 91663 | 155652 | 240727 | 263000 | 285134
mTCP | 316345 | 468220 | 765612 | 1130000 | 1489540
Linux-3.13.0
Intel Xeon E5-2690
32 GB RAM
Intel 10 Gbps NIC (Niantec)
Notes: To determine whether the Linux kernel is really the bottleneck, we conducted an experiment on a TCP server that ping pong’s 64B messages to the client. We run this experiment with (1) Linux, (2) Linux w/ SO_REUSEPORT socket option (which is multi-core friendly), and (3) mTCP. We clearly see that neither Linux versions improve performance as # of cores are increased. On the other hand, mTCP-enabled application server shows a linear growth in performance as more cores are assigned to it.

## Slide 9: Overview of node.js/mTCP-DPDK
NIC Device
mTCP thread 0
User-level DPDK I/O
Symmetric RSS (H/W)
Per-core NIC queue
mTCP thread 1
User-level DPDK I/O
Core 0
Core 1
Per-core listening queue
H/W-level
S/W-level
Notes: This is an example design of the mTCP-version of node.js (2-core setup) system. Each core runs its own independent instance of node.js.
We make sure that packets that enter the system are processed in the same core throughout the lifetime of the connection. Packets are distributed across NIC queues using symmetric RSS algorithm. The packets are handled first in the mTCP thread where packet I/O & TCP/IP state management is done before the payload is passed to the node.js application thread. Each core has its own dedicated listening queue and its own file descriptor queue. This dual-thread architecture per CPU core ensures that the application thread does not starve time-critical mTCP tasks such as ACK responses, timeouts etc.

## Slide 10: Exploiting Batched + Prioritized Event/Packet Processing
Accept
queue
S
S/A
F/A
Data list
ACK list
Control list
TX manager
Connect
queue
Application thread
SYN
RST
FIN
Data list
Write
queue
Close
queue
write()
Rx manager
Payload handler
Socket API
Internal event queue
Event
queue
ACK list
Control list
TX manager
connect()
close()
epoll_wait()
accept()
SYN
ACK
Data
Rx queue
Tx queue
mTCP thread
SYN | Synchronize TCP sequence numbers (start TCP conn.)
RST | Reset the connection (terminate TCP conn.)
FIN | Last packet from sender
ACK | TCP acknowledgement
DPDK introduced concept of L2-/L3- tiered batching
We extend batching all the way up to app (L7) layer
Prioritization enhances total link utilization of the Ethernet link.
Notes: mTCP stack implements a number of optimizations. For this talk, only 2 are explained.
1- First, it aggressively employs batching. User-space network I/O drivers such as DPDK provide batching (of packets) support up to L2/L3 layer(s). We extend this support up to L7 (app layer). In this example, we show that payloads (or events) of two different flows are grouped together in the Event queue and then passed in batch to the application layer via epoll_wait() function call.
2- We also provide prioritization of traffic. Outgoing control packets such as SYNs, RSTs, and FINs are grouped together in a higher priority queue (when compared to TX data packets). The control list is emptied (i.e. transmitted from the NIC) first before sending out data packets. This can prove to be a useful optimization tweak since control packets can potentially influence the TCP send/recv window parameters of the connection (that eventually affect the Ethernet link utilization).

## Slide 11: Context Switching?
n
BSD socket layer
Kernel TCP
Packet I/O
mTCP socket layer
mTCP thread
DPDK I/O
User
Kernel
Context switching
Thread switching
higher overhead
<
Batching to amortize thread switch overhead
Node.js (vanilla)
Node.js (mTCP)
Notes: Since the application including the TCP/IP stack and NIC operations are in user space, kernel  user context switching is skipped. We make sure that the incoming packets are processed in batches. Also, system call invocation overhead is more than the thread switching overhead (in terms of CPU cycles spent).

## Slide 12: Performance Evaluation: File Download
Chart: Downloading a small file (17 B)
| 100 | 500 | 1000 | 2000
Linux-KBps | 385 | 391 | 407 | 408
mTCP-KBps | 950 | 1017 | 1006 | 665
*Concurrency*: # of client connections at any given time
2.5x
Single CPU
Intel Xeon E5-2699 v4 @ 2.20 GHz (max: 3600 MHz)
56 MB L3 cache
22-per-core dual-node processor
65 GB RAM
Bottleneck = Client
(uses Linux stack)
Notes: On Intel BDX, using only 1 core, we show our first evaluation result. On the X-axis is the concurrent flow number; on the Y-axis is the throughput. You can clearly see that mTCP-based application shows almost 2x performance improvement in the best case. For x = 2000, the performance does not scale as well. This is because the TCP client used to benchmark the node.js server uses the traditional Linux kernel for networking. This proves to be the bottleneck.

## Slide 13: Performance Evaluation – MongoDB Test
Chart: MongoDB test
| 1p | 2p | 4p | 8p | 16p
100 | 0.87683 | 1.7669 | 1.3791 | 1.151 | 1.0292
512 | 0.81252 | 1.6559 | 1.4973 | 1.2327 | 1.1873
1024 | 0.87678 | 1.4523 | 1.5148 | 1.2126 | 1.2017
2048 | 0.83762 | 1.2001 | 1.1666 | 1.1597 | 1.1718
4096 | 0.77347 | 1.0521 | 1.127 | 1.1183 | 0.9935
8192 | 0.71471 | 1.1997 | 1.1708 | 1.1025 | 0.98132
Concurrency Levels
Intel Xeon E5-2699 v4 @ 2.20 GHz (max: 3600 MHz)
56 MB L3 cache
22-per-core dual-node processor
65 GB RAM
Node.js w/ mTCP
Node.js client
HTTP GET
HTTP Response
Fetch DB Record
Send DB Record
1
2
3
4
MongoDB w/ Linux
Flow Size: 2K
Performance improvement up to 1.8x
Bottleneck = MongoDB
(Linux stack)
Notes: This experimental result shows the multi-core performance. The test results are the evaluation numbers of the node.js-specific microbenchmarks.
The figure on the right describes a node.js cluster. In this setup, the client requests a retrieval of a DB record. The node.js/mtcp-based relays this request to the database server (running MongoDB server). The response is then prepared by the node.js server (after getting the record back from the DB server).
The X-axis shows the performance improvement of mTCP-based version over vanilla-based version. The X-value “1.00” shows the baseline performance. Values >= 1.00 show the performance improvement provided by the mTCP-based node.js server over its vanilla-based alternative (linux) version. The Y-axis shows the # of cores (processes) being used.
Why is the performance not improving as number of processes increase? The MongoDB server is the bottleneck! Our detailed profiling results show that the inflated response latencies are coming due to the slow-performing MongoDB is the culprit.
Figure 12 of our paper: https://ajamshed.github.io/papers/nsdi14-jeong.pdf show that mTCP-based applications show performance improvement in proxy-like settings. Figures 7(a), 8, and 10 in the same paper show that mTCP-based applications show scalable performance improvement. These results further back our claim that MongoDB stack needs improvement (with regards to performance) in this setup.

## Slide 14: Summary of Transfer Plan
IL, & partners, initiate mTCP transfer to Linux Foundation (pre Gate 3)
mTCP stack for node.js (libc-wrapper)
  Source code
  Documentation
  Micro-benchmarks
  Testsuite
SSG Plan (post Gate 3)
  Initiate pull request to the community for the integrated mTCP/node.js stack
Q2 2019 (Gate 3)
Notes: This is the outline of the transfer plan.
We plan to move mTCP under the umbrella of Linux Foundation and publish the mTCP code to public before Gate 3.
We plan to transfer the source code, documentation, micro-benchmarks and testsuite by Q2 2019, which also happens to be our projected Gate 3 transfer target.
FYI: Node.js is open-source
The SSG/OTC/DSCP team plans to initiate a pull request on node.js repo thereafter.

## Slide 15: IL Gate 2 Checklist: Transition POC  Transfer
√ | Criteria | Considerations/Questions | Notes
√ | Quality of the Transfer Plan | In what form is the result to be delivered? Have we bounded the scope and expectations for the transfer? How do we manage joint work? What is the timeline and how do we know when Intel Labs is done? | mTCP-libc-wrapper will be available publicly on the github site.
√ | Certainty of a BU intercept | Are we certain there is a clear intercept to BU processes or products for the technology we are transferring? | The SSG/OTC Node.js team is planning to push a software patch merge request.
√ | Competitive Position | Has the competitive position been tested both internally and externally? Is there a clear articulation of Intel value and a clear definition of success? | Leading packet processing libraries for IA. Competitive position is understood. Enhanced networking performance is desired in node.js community.
√ | Ecosystem Engagement | Is additional ecosystem engagement required? What is IL’s / BU’s role during the transfer phase? | Yes. SSG engagement is needed to move node.js applications to support mTCP.
√ | Business Plan | Does the business unit have a go-to-market plan for this technology transfer? | mTCP is a key ingredient to accelerate various applications, in this case Node.js
√ | Intellectual Property | Have key invention disclosures and/or patents been filed? What additional filings are needed? Has the PoC IP been uploaded to a secure repository such as the Research Reuse Repository or Secure Git? | Yes. The libc-wrapper-branch is in the secure Intel github site.
 | Compliance | Have you completed the compliance questionnaire in your Workstream deliverable and aligned expectations with the BU? Include backup slide with screenshot of compliance summary and link to details. | Process started, will be done by Gate-3.
√ | RAPID Model | R: IL Transfer Owner (with Lab Director support) D: Managing Director of Intel Labs A: Senior BU Transfer Owner I: Intel Labs Staff P: Project Team | See 2nd slide.
Transfer to Intel Business Unit
Transfer to External Ecosystem (with BU Biz Value & Approval)
Select Type:
√
Notes: Copy the checkmark from the header of the left column into each row for which the criteria has been met. Document any key notes for discussion in the right column.

## Slide 16: Feedback
Thanks!

## Slide 17: Intel Labs Workstream Appendix

## Slide 18: Corporate Compliance Summary for mTCP : Multi CPU Core TCP
For detailed compliance questions, answers, and additional info (files, links...) Click here

## Slide 19: Node.js Runtime Engine (2nd version)
Node.js
Node.js Bindings (C++)
<socket, http parser…>
V8 (C++)
Libuv (C)
Node.js Application (JavaScript)
Libuv (C)
Event task queue
open(…)
send(…)
read(…)
…
…
Worker thread pool
Event loop
dispatch
trigger
callback
Notes: Libuv accepts service requests from V8 and Node.js bindings substrate and enqueues them in the event task queue
The main event loop sequentially executes all pending tasks enlisted in the task queue. All blocking calls are handed over to the worker threads. All others (including networking I/O tasks) are handled by the event thread.

## Slide 20: Node.js (3rd version)
Node.js
Node.js Bindings (C++)
<socket, http parser…>
V8 (C++)
Libuv (C)
Cross platform asynchronous I/O event loop + worker thread pool + …
Node.js Application (JavaScript)
OS Kernel
JavaScript event-driven, non-blocking runtime engine
  Fast, scalable network application services
Widespread client base
Notes: Node.js is a fast scale-able server run time engine
The server application can be written in JavaScript
Node.js is widely being used across the industry. Some of its customers include LinkedIn, Uber, Netflix, Trello, NASA, Walmart and PayPal.
Node.js is composed of 4 components.
  1. The application section contains the JavaScript code that runs the server application logic.
  2. V8 is the open source module that interprets the JS code with the help of JavaScript runtime engine that converts JavaScript bytecode to machine language at run-time.
  3. Node.js bindings is the shim layer that acts as a go-between for the network I/O layer, file system I/O calls etc.
  4. libuv is a third party library that is responsible for I/O tasks including network communication

## Slide 21: Intel Labs Workstream Why is the kernel networking stack slow?

## Slide 22: Broken CPU Cache Locality
1. Broken locality
Per-core packet queue
Receive-Side Scaling (H/W)
Core 0
Core 1
Core 3
Core 2
Interrupt handler +
TCP state
management
accept() read() write()
Interrupt handling core != accepting core
Notes: In the first example, we see that one core handles the RX interrupt while another core handles TCP-specific RX operations.
Since the interrupt handling core is different than the accepting core, there is a necessary L2/L3 cache miss (depending on CPU core configuration).
More comments on slide 5.

## Slide 23: Lack of Support for Batch Processing
2. Per packet, per system call processing
Inefficient per packet processing
Frequent mode switching Cache pollution
Per packet memory allocation
Inefficient per system call processing
accept(), read(), write()
Packet I/O
Kernel TCP
Application process
BSD socket
Linux epoll
Kernel
User
Notes: Second example,
Each packet goes through an expensive (thick) kernel-resident networking stack. There is also a necessary kernel user space context switch. Memory allocation per packet as well as the amount of CPU cycles spent on packet processing in the stack leads to frequent mode switching and CPU cache pollution.
More comments on slide 6.

## Slide 24: Shared File Descriptors Increase Contention
0. Shared resources
  Shared listening queue
  Shared file descriptor space
Notes: Ongoing TCP connections are handled through file descriptors that are normally a shared resource across CPU threads.
First, they share a common listening queue which is used to accept incoming connection requests.
Second, file descriptors are shared across threads.
THIS SLIDE IS DEPRECATED.

## Slide 25: Shared File Descriptors Increase Contention
Per-core packet queue
Receive-Side Scaling (H/W)
Core 0
Core 1
Core 3
Core 2
Listening queue
Lock
File descriptor space
Linear search for finding empty slot
Notes: In this example we show ingress traffic being split across NIC RSS queues.
All threads contend for the listening queue to accept new connection requests (resource contention)
To establish a connection, each thread needs to scan the file descriptor space to look for an empty (available) file descriptor. This is an expensive operation.
THIS SLIDE IS DEPRECATED.

## Slide 26: Intel Labs Workstream Evaluation results (alternative)

## Slide 27: Performance Evaluation - II
Flow Size: 2K
Chart: Micro-Service Use Case
| 1p | 2p | 4p | 8p | 16p
2048 | 0.95288 | 1.704 | 1.4373 | 1.5304 | 1.9462
4096 | 0.89517 | 1.5813 | 1.5158 | 1.7918 | 1.7689
8192 | 0.86721 | 1.3487 | 1.447 | 1.8188 | 1.9552
Chart: MongoDB test
| 1p | 2p | 4p | 8p | 16p
100 | 0.87683 | 1.7669 | 1.3791 | 1.151 | 1.0292
512 | 0.81252 | 1.6559 | 1.4973 | 1.2327 | 1.1873
1024 | 0.87678 | 1.4523 | 1.5148 | 1.2126 | 1.2017
2048 | 0.83762 | 1.2001 | 1.1666 | 1.1597 | 1.1718
4096 | 0.77347 | 1.0521 | 1.127 | 1.1183 | 0.9935
8192 | 0.71471 | 1.1997 | 1.1708 | 1.1025 | 0.98132
Performance improvement up to 1.96x
baseline
Concurrency Levels
Concurrency Levels
Flow Size: 2K
Notes: On Intel BDX, this graph shows the multi-core performance. The 2 test results are the evaluation numbers of the node.js-specific microbenchmarks.
The left figure shows a node.js cluster. The X-axis shows the performance improvement. The Y-axis shows the # of cores (processes) being used….
Why is the performance not improving as number of processes increase? The MongoDB server is the bottleneck!

## Slide 28: Intel Labs Workstream References

## Slide 29: Related Papers
Eunyoung Jeong, Shinae Woo, Muhammad Jamshed, Haewon Jeong, Sunghwan Ihm, Dongsu Han, KyoungSoo Park. “mTCP: a Highly Scalable User-level TCP Stack for Multicore Systems, ” in the 11th USENIX Symposium on Networked Systems Design and Implementation (NSDI '14), Seattle, WA, USA, Apr 2-4, 2014.
  NSDI Community Award
Muhammad Jamshed, YoungGyoun Moon, Donghwi Kim, Dongsu Han, KyoungSoo Park. “mOS: A Reusable Networking Stack for Flow Monitoring Middleboxes,” in the 14th USENIX Symposium on Networked Systems Design and Implementation (NSDI '17), Boston, MA, USA, Mar 27-29, 2017.
  NSDI Best Paper Award
Muhammad Jamshed, Donghwi Kim, YoungGyoun Moon, Dongsu Han, KyoungSoo Park. “A Case for a Stateful Middlebox Networking Stack,” in the SIGCOMM Computer Communication Review. Rev. 45, Pg 355-356, Aug, 2015.
Notes: mTCP and its follow-up projects have yielded a number of research papers in leading networking conferences.

## Slide 30: Other mTCP-based Applications

## Slide 31: mTCP-based Applications
Application | Description | Modified lines / Total lines
Lighttpd | An event-driven web server | 65 / 40K
ApacheBench | A webserver performance benchmark tool | 29 / 66K
SSLShader | A GPU-accelerated SSL proxy [NSDI ’11] | 43 / 6,618
WebReplay | A web log replayer | 81 / 3,366
Notes: A number of well-known applications have been ported to mTCP. Here are a few.
Lighttpd: https://www.lighttpd.net/
ApacheBench: https://httpd.apache.org/docs/2.4/programs/ab.html
SSLShader & WebReplay are in-house software artifacts that were not released to general public.

## Slide 32: mTCP API

## Slide 33: mTCP Socket API
/* socket creation, bind, listen functions */
int socket(int domain, int type, int protocol); int bind(int sockid, const struct sockaddr *addr, socklen_t addrlen); int listen(int sockid, int backlog);
/* accept and connect */ int accept(int sockid, struct sockaddr *addr, socklen_t *addrlen); int connect(int sockid, const struct sockaddr *addr, socklen_t addrlen);
/* read functions */
int read(int sockid, char *buf, int len);
int readv(int sockid, struct iovec *iov, int numIOV);
/* write functions */
int write(int sockid, char *buf, int len); int writev(int sockid, struct iovec *iov, int numIOV);
/* socket closure */
int close(int sockid); int mtcp_abort(mctx_t mctx, int sockid);
/* rss queue mapping */
int mtcp_init_rss(mctx_t mctx, in_addr_t saddr_base, int num_addr, in_addr_t daddr, in_addr_t dport);
Notes: - Sample socket API. (closely follow BSD socket interface).

## Slide 34: Sample Server Code
static void thread_init(ctx_t mctx)
{
/* init declarations */
int sock, lsock, ep, i;
struct sockaddr_in saddr;
struct epoll_event ev, events[MAX_EVENTS];
/* create listening socket */
lsock = socket(AF_INET, SOCK_STREAM, 0);
/* bind and listen to a specific port */
saddr.sin_family = AF_INET; saddr.sin_addr = INADDR_ANY;
saddr.sin_port = htons(80);
bind(lsock, (struct sockaddr *)&saddr, sizeof(struct sockaddr_in));
listen(lsock, 4096);
/* create epoll queue & enlist listening port in epoll queue */
ep = epoll_create(MAX_EVENTS);
ev.events = EPOLLIN; ev.data.sockid = lsock;
epoll_ctl(ep, EPOLL_CTL_ADD, lsock, &ev);
while (1) {
int nevents = epoll_wait(ep, events, MAX_EVENTS, -1);
for (i = 0; i < nevents; i++) {
if (events[i].data.sockid == lsock) {
sock = accept(lsock, NULL, NULL);
...
} else if (events[i].events == EPOLLIN) {
read(...);
...
}
}
}
}

## Slide 35: Sample Client Code
static void thread_init(ctx_t mctx)
{
int sock, lsock, ep, i; /* init declarations */
struct in_addr_t saddr, daddr; struct in_port_t sport, dport;
struct epoll_event ev, events[MAX_EVENTS];
saddr = INADDR_ANY; daddr = inet_addr(DHOST_IP);
dport = htons(80);
/* initialize per-thread client-port RSS pool */
mtcp_init_rss(mctx, saddr, 1, daddr, dport);
ep = epoll_create(MAX_EVENTS);
while (1) {
if (connection_count < conn_thresh)
CreateConnection(mctx, ep); /* connect() */
int nevents = epoll_wait(ep, events, MAX_EVENTS, -1);
for (i = 0; i < nevents; i++) {
if (events[i].events & EPOLLIN)
HandleReadEvent(...); /* read() */
...
}
}
}

## Slide 36: mTCP Socket API
/* configuration file reading */
int mtcp_init(char *config_file); void mtcp_destroy(); int mtcp_getconf(struct mtcp_conf *conf); int mtcp_setconf(const struct mtcp_conf *conf); int mtcp_core_affinitize(int cpu);
/* thread context manipulation */
mctx_t mtcp_create_context(int cpu); void mtcp_destroy_context(mctx_t mctx); typedef void (*mtcp_sighandler_t)(int); mtcp_sighandler_t mtcp_register_signal(int signum, mtcp_sighandler_t handler);
/* pipe, getsock/setsockopt, set fd non-blocking mode */ int mtcp_pipe(mctx_t mctx, int pipeid[2]); int mtcp_getsockopt(mctx_t mctx, int sockid, int level, int optname, void *optval, socklen_t *optlen); int mtcp_setsockopt(mctx_t mctx, int sockid, int level, int optname, const void *optval, socklen_t optlen); int mtcp_setsock_nonblock(mctx_t mctx, int sockid);
/* mtcp_socket_ioctl: similar to ioctl, but only FIONREAD is supported currently */ int mtcp_socket_ioctl(mctx_t mctx, int sockid, int request, void *argp);

## Slide 37: mTCP CPU-Queue Assignment

## Slide 38: CPU Queue Assignment
1. Default (RSS-based)
Per-core packet queue
Receive-Side Scaling (H/W)
q 0
q 1
q 1
q 0
Core 0
Core 1

## Slide 39: CPU Queue Assignment
2. Port-filter
Per-core packet queue
Receive-Side Scaling (H/W)
q 0
q 1
q 1
q 0
Core 0
Core 1
Core 2
Core 3
TCP List-port: w
TCP List-port: x
TCP List-port: y
TCP List-port: z
w
x
y
z

## Slide 40: mTCP configuration file (1)
# The underlying I/O module you want to use. Please enable only one out of the two.
#io = netmap
io = dpdk
# No. of cores setting (enabling this option will override the `cpu' config for those applications that accept
# num_cores as command line arguments). E.g. in case ./epserver is executed with `-N 4', the mtcp core will still
# invoke 8 mTCP threads if the following line is uncommented.
#num_cores = 8
# Core mask
#core_mask = 00000F0F0 (option 1)
#core_mask = 4-7 12-15 (option 2)
# NIC Queue Function. Default is symmetric RSS.
#queue_func = rss
queue_func = port_filter
# Number of memory channels per processor socket (dpdk-only)
num_mem_ch = 4
# Enable multi-process support
#multiprocess = 1
# Used port (please adjust accordingly)
port = dpdk0
#port = dpdk0 dpdk1
Notes: Sample mTCP startup configuration file
  Please see the comments in the slide

## Slide 41: mTCP configuration file (2)
# Maximum concurrency per core (default = 10000)
max_concurrency = 8192
# Maximum number of socket buffers per core (default = 10000)
# Set this to small value if there are many idle connections
max_num_buffers = 8192
# Receive buffer size of sockets; if not set: rcvbuf = sndbuf
rcvbuf = 8192
# Send buffer size of sockets; if not set: sndbuf = rcvbuf
sndbuf = 8192
# if sndbuf & rcvbuf not set: sndbuf = rcvbuf = 8192
# TCP timeout seconds
# (tcp_timeout = -1 can disable the timeout check)
tcp_timeout = 30
# TCP timewait seconds
tcp_timewait = 0
# Interface to print stats (please adjust accordingly)
# You can enable multiple ports in separate lines
stat_print = dpdk0
#stat_print = dpdk1
Notes: Sample mTCP startup configuration file
  Please see the comments in the slide

## Slide 42: mTCP Implementation

## Slide 43: mTCP Implementation
12,727 lines in C code
  Packet I/O, TCP flow management, user-level socket API, event system library
Supports Intel DPDK
  Fast packet I/O library + event-driven packet I/O
  Originally based on PacketShader IOEngine [SIGCOMM’10]
TCP protocol conformance
  Follows RFC793
  Congestion control algorithm: NewReno
Passing correctness test and stress test with Linux TCP stack

## Slide 44: Intel Labs Workstream Follow-up works

## Slide 45: Follow-up projects within Intel
User Interrupts* (IL, Systems Architecture Lab)
  Issue: mTCP thread uses DPDK PMD
    May starve the application
  Solution: Deliver I/O interrupts directly to target DPDK PMD thread
    New instruction (UIRET, similar to a near RET) to return from user-interrupt handling
    User-interrupt masking provided by UIF – analogous to EFLAGS.IF
    ISA extensions allow OS to manage user interrupts for each user thread
Redis-mTCP (DCG, Visual Wrklds & Accel group)
  Issue: Performance chokes up with increasing # of client requests (bottleneck = network module)
  Solution: Replace Linux kernel networking stack with mTCP
    Preliminary evaluation: > 2x improvement in performance
* Content borrowed from Scott Diaz’s slide deck